## Slide 1
Determination of PDH Modulation Frequency
Daisuke TATSUMI
National astronomical observatory of Japan
#-----------------------------------------------------------------------
# pdh-signal.kat test file for Finesse 1.1
# (Error signal of the Pound-Drever-Hall signal)
#
# http://www.gwoptics.org/finesse/
# 01.11.2013
#
# The "#" is used for comment lines.
#
#
# m1 m2
# .-----. .-. .-.
# | | | | . . . . . . . . . . | |
# --> n1 | EOM | n2 n3 | | n4 . s_cav . n5 | |
# | | | | . . . . . . . . . . | |
# `-----' | | | |
# `-' `-'
#------------------------------------------------------------------
finesse: Frequency domain INterfErometer Simulation SoftwarE
http://www.gwoptics.org/finesse/

## Slide 2
l i1 1 0 n0 # laser P=1W f_offset=0Hz
s s0 1 n0 n1
mod eo1 30M 0.1 3 pm n1 n2 # phase modulator f_mod=15MHz
# midx=0.1 order=1
s s1 1 n2 n3
# a Fabry-Perot cavity
m m1 0.92 0.08 0 n3 n4 # mirror R=0.92 T=0.08 phi=0
s s_cav 0.037474 n4 n5 # space L=37.474mm
m m2 0.9995 0.0005 0 n5 dump # mirror R=0.9995 T=0.0005 phi=0
pd1 inphase 30M 0 n3 # photo diode + mixer
# f_demod=15MHz phase=0
pd1 quadrature 30M 90 n3 # photo diode + mixer
# f_demod=15MHz phase=90degrees
xaxis m2 phi lin -90 90 400 # xaxis: tune mirror m2
# from -90 to 90 (400 steps)
yaxis abs # plot `as is'

## Slide 3
FSR (Free Spectral Range)
FSR = c /2L
c: light speed
L: cavity length
FSR = 4GHz
--> L = c /2 /FSR = 37.474 mm
Finesse
r1 = sqrt(R1) = sqrt(0.92) = 0.95917
r2 = sqrt(R2) = sqrt(0.9995) = 0.99975
Finesse = 74.8998
FWHM of the cavity
FWHM = FSR / finesse = 4 GHz / 75 = 53.4 MHz

## Slide 4
> ./finesse SHG.param
[INPUT]
Length= 3.747400e-02
R1= 9.200000e-01
L1 = 0.000000e+00
R2 = 9.995000e-01
L2 = 0.000000e+00
[OUTPUT]
Finesse = 74.8998
FSR = 4.000006e+09
FSR/Finesse = 5.340477e+07
Gain = 4.742051e+01
Reflectivity = 0.97629
Transmissivity = 2.371025e-02
> ./finesse SHG.param
[INPUT]
Length= 3.747400e-02
R1= 9.200000e-01
L1 = 1.000000e-04
R2 = 9.995000e-01
L2 = 1.000000e-04
[OUTPUT]
Finesse = 74.8998
FSR = 4.000006e+09
FSR/Finesse = 5.340477e+07
Gain = 4.736123e+01
Reflectivity = 0.97629
Transmissivity = 1.894449e-02

## Slide 6
PDH signal get lower than that of optimal.
< FWHM = 60 MHz